## Slide 1
NEEV / STARTUP CONCEPT
SPACE PILOT
Intelligence for every space.
A compact device that controls electricity or electrical appliances based on the presence of person in a room and switches connected room equipment ON or OFF—without Wi-Fi.
SENSE • COUNT • SWITCH
Presented by: __Team Nova __

## Slide 2
01 / THE PROBLEM
A room's occupancy changes. Its systems need context.
A room can be busy, empty, then busy again throughout the day.
SPACEPILOT • NEEV PROJECT
EXAMPLE: A CLASSROOM DURING THE DAY
08:00
Class begins
Occupied
10:00
Break
May be empty
10:15
Next lesson
Occupied
15:00
School ends
Empty
The management gap
People may need to notice when a space changes from occupied to empty and act accordingly.
The opportunity
Could a room provide a reliable occupancy signal and use it to manage selected systems consistently?

## Slide 3
02 / EXAMPLE SCENARIO
SpacePilot in a coaching-centre classroom
This example shows how SpacePilot switches a connected light or fan based on estimated room occupancy.
SPACEPILOT • NEEV PROJECT
BEFORE CLASS
Room is empty. Estimated count is 0; the connected load is OFF.
STUDENTS ENTER
The doorway sensors detect entry and update the count; the first entry switches the load ON.
CLASS IN SESSION
As long as the estimated count stays above zero, the connected load remains ON.
EVERYONE LEAVES
When the count returns to zero, the controller waits briefly, then switches the load OFF.
Core idea
Estimated occupancy becomes an input for decisions about selected equipment.

## Slide 4
03 / THE SOLUTION
What exactly is SpacePilot?
SpacePilot is an automatic occupancy-controlled switch—not a Wi-Fi or smart-appliance system.
SPACEPILOT • NEEV PROJECT
SPACEPILOT
1. Detect a doorway crossing
2. Determine entry or exit
3. Update the estimated count
4. Switch the connected load
In one sentence
SpacePilot uses two doorway sensors and a small controller to estimate occupancy, then operates a relay or switching module to turn a connected light or fan ON/OFF locally.
No Wi-Fi required: first entry → ON; last exit → short delay → OFF.

## Slide 5
04 / THE MECHANISM
How can it tell whether someone entered or exited?
Two sensors are placed a short distance apart across the doorway.
SPACEPILOT • NEEV PROJECT
OUTSIDE
INSIDE THE ROOM
Sensor A
Sensor B
ENTRY: A → B
EXIT: B → A
Entry sequence: A then B
The controller interprets the order as a person moving into the room.
Exit sequence: B then A
The reverse order is interpreted as a person leaving.
The order of sensor events provides direction; one sensor alone cannot reliably tell which way a person crossed.

## Slide 6
05 / OCCUPANCY LOGIC
How the estimated people count changes
The controller keeps a running count based on confirmed crossing sequences.
SPACEPILOT • NEEV PROJECT
START
0
EMPTY
ENTRY
1
OCCUPIED
ENTRY
2
OCCUPIED
EXIT
1
OCCUPIED
EXIT
0
POTENTIALLY EMPTY
If count > 0
The room is treated as occupied.
If count = 0
The system can wait briefly before applying empty-room rules.

## Slide 7
Process in 5 Steps
From a person crossing the doorway to a connected appliance switching automatically.
1
DETECT CROSSING
A person interrupts the first sensing beam.
2
IDENTIFY DIRECTION
A → B = entry | B → A = exit.
3
UPDATE COUNT
Entry +1 | Exit −1 | never below zero.
4
CHECK ROOM STATE
Count above zero = occupied; zero = potentially empty.
5
SWITCH THE LOAD
Count above zero = ON. Count at zero = wait briefly, then OFF.
Key logic: sensor order determines direction; the estimated count controls the local switch.

## Slide 8
07 / WHAT IT CONTROLS
Estimated occupancy directly controls a connected load
A local controller and switching module can operate a compatible light or fan without Wi-Fi.
SPACEPILOT • NEEV PROJECT
Occupancy state
EMPTY or OCCUPIED, based on the estimated count and the configured OFF delay.
Control rules
Count above zero: switch ON. Count returns to zero: wait briefly, then switch OFF.
User override
A manual override can let an authorised person keep the load ON or OFF when needed.
OPTIONAL SAFEGUARDS / FUTURE OPTIONS
• Short delay before switching OFF • Manual override switch • Status indicator • Optional presence verification if testing shows it is needed • Wi-Fi / multi-room reporting is not required for the first version

## Slide 9
06 / WHAT WE WOULD BUILD
The main parts of the first demonstration
A low-voltage demonstration proves the sensing, counting and automatic switching logic.
SPACEPILOT • NEEV PROJECT
1
Doorway sensors
Detect the order of crossings.
2
Microcontroller
Processes events and updates the count.
3
Relay / switch module
Switches the connected demonstration load ON or OFF.
4
Demo output
A small low-voltage lamp or 5V fan demonstrates the switch.
First version
No Wi-Fi, app or cloud dashboard is required for the first version.

## Slide 10
08 / WHO MIGHT USE IT
Start with places that manage many shared rooms
The first target customer should be narrow enough for us to interview and test with.
SPACEPILOT • NEEV PROJECT
Schools & coaching centres
Multiple classrooms, repeated schedules and a clear person responsible for room operations.
Offices & meeting rooms
Spaces that switch between occupied meetings and empty periods.
Hostels & shared facilities
Common spaces whose usage changes throughout the day.
FIRST CUSTOMER HYPOTHESIS
A facility with several rooms, recurring occupancy patterns and someone who can approve a small pilot.

## Slide 11
09 / BUSINESS OPPORTUNITY
A product that could scale room by room
Begin with one useful unit, prove it, then expand only if customers see value.
SPACEPILOT • NEEV PROJECT
Hardware kit
A room-level controller with doorway sensors and a compatible control interface.
Installation & setup
Configure the unit and test it in the customer's actual room.
Future multi-room service
Optional reporting, monitoring and maintenance if customers need them.
A REALISTIC PATH
Interview → build a low-voltage demo → test accuracy → run a pilot → decide whether to scale.

## Slide 12
Applications & Key Benefits
Designed for shared spaces where compatible equipment is often left running unnecessarily.
WHO COULD USE SPACEPILOT?
01
Schools & colleges
Classrooms, labs and teaching rooms.
02
Coaching centres
Between-class rooms and study areas.
03
Offices & meeting rooms
Shared rooms used throughout the day.
04
Libraries & study rooms
Common spaces with lights and fans.
KEY BENEFITS
ENERGY EFFICIENCY
Can reduce avoidable appliance runtime.
AUTOMATIC OPERATION
Less reliance on manual switching.
OCCUPANCY ESTIMATE
Provides a running estimate, not a guaranteed count.
COMPACT INSTALLATION
Both sensors designed for one enclosure.
POTENTIAL COST REDUCTION
Actual savings must be measured in testing.

## Slide 13
SPACEPILOT / THE IDEA
A room should know when it is in use.
SpacePilot estimates occupancy from doorway crossings and locally switches a connected light or fan ON when someone is inside, then OFF after the room is empty.
SENSE → COUNT → SWITCH
THANK YOU
Questions & discussion